## Slide 1: Automotive Battery Thermal Runaway Prediction: EIS Project
Robert Tan & Dr. Wesley Poh
Automotive Division – Global Systems Team
Infineon Technologies Asia Pacific Pte Ltd

## Slide 2: Objectives
The primary objective is to conduct rigorous testing to gather datasets for developing a predictive model capable of identifying early warning signs (precursors) of thermal runaway in lithium-ion cells before catastrophic failure occurs. The project will utilise controlled battery cycling to induce degradation and capture high-resolution electrochemical data for analysis, as elaborated below.
i) Experimental Set-Up and Safety
- Test Bench Construction: Set-up of battery cyclers (Chroma & NGI) and environmental chambers.
- Sensor Integration: Installation of thermocouples, voltage sensors, and strain gauges (if monitoring swelling) on target cells.
- Safety Protocols: Implementation of containment vessels and fire suppression systems to manage intentional or accidental thermal events during testing.
ii) Data Generation (Cycling Regimes)
- Baseline Characterisation: Perform initial capacity and impedance checks on fresh cells.
- Accelerated Aging: Subject cells to high C-rate cycling and elevated temperatures to accelerate degradation.
- Abuse/Trigger Testing*: Apply controlled overcharge or overheating protocols to push cells toward the “onset” of thermal runaway, capturing near-failure data. *Constraint: Testing will cease immediately upon detection of thermal runaway initiation (venting or rapid temperature rise) to preserve data integrity.
iii) Data Analysis and Modelling
- Extract key features from raw battery data, such as coulombic efficiency trends, differential voltage analysis, and temperature rate of change. These will be used to develop machine learning learning models for predicting thermal runaway precursors.

## Slide 3: Nyquist plot from EIS (electrochemical impedance spectroscopy)
higher Hz range
Lower Hz range
mid Hz range
Impedance spectrum of a Li-Ion battery vs frequency coverage
mHz range
Relevant for SoX*
mHz till Low Hz range
  Gen1 EIS TLE9012DQU
mHz till Mid Hz range
  Gen2 EIS TLE9018DQK
Higher frequencies
  Gen3/4 EIS TLE9024DQK/TLE90xxEQK
Low Hz range
Mid Hz range
High Hz range
The higher the impedance frequency, e.g., 1 kHz, the more crosstalk effects of the wiring of the battery cell itself are overlaying the measurement.
SoH is the source for SoC algorithm calibration over aging and power estimations. Hence, EIS implementation for SoH is valuable.
*Depending on cell chemistry, structure,
use case, etc.
Relation – Impedance spectrum vs EIS use case
SoH
SoC
Temp
Power
*Depending on cell chemistry, structure,
use case, etc.

## Slide 4: Using EIS data from aging cells
Characterisation of cells in frequency and time domain
Model parameterisation and algorithm development
From aging data to model…
Measured vs. simulated CC/CV charge profiles to validate electrochemical model
Detection of safety critical lithium plating side reaction with EIS
Cycling aging tests with EIS meas. during reference performance tests (RPTs)
Aging tests on NMC cells aim to identify aging-sensitive cell parameters via EIS.
Validation of a real-time model running on AURIX.
Detection of lithium plating using EIS.

## Slide 5: Types of EIS in HV batteries and our available solutions
Pack-Level EIS
Rsense
R1
R2
Excitation
Circruit
PSOCTM SPM
2
3
4
Vsense
5
6
Isense
PWM
1
Vdd
AC decoupling circuit
Requires V/I sensing of the pack only.
Typically performed by the pack montoring IC.
Typically performed for intercept-point (typically high Hz) ranges for estimating State-of-Power.
Available Infineon Solutions:
PSOCTM SPM: Pack monitoring IC with High-Voltage Precision Analog and capability to measure up to 10 kHz pack EIS.
Cell-Level EIS
Requires V/I sensing of every individual cell.
Can be performed using single-channel AFE, multi-channel AFE, or highly synchronous AFEs.
Typically performed for mHz to mid-Hz ranges due to challenging cross-talking and magnetic coupling.
TLE90xx
1
2
3
Vsense
4
5
Isense
Rsense
Rload
Current Excitaion
Available Infineon Solutions:
TLE9010: Single-channel EIS with AC-decoupled ADC and capability to measure up to 7 kHz EIS.
TLE9018 + PSOCTM HVPA: Synchronous EIS measurement with Iso UART (up to 333 Hz).

## Slide 6: EIS Demo
1
3
2
Trigger measurement
Read results and compute EIS
Perform synchronous V and I measurement

## Slide 7: High-Voltage (HV) BMS
AFE 1
(TLE901x)
BMU
- +
- +
- +
- +
HV+
- +
- +
- +
- +
- +
- +
Shunt
HV-
UART/SPI
CAN
CAN Transceiver
PMIC
CMU1
AFE 2
(TLE901x)
CMU2
AFE 3
(TLE901x)
CMU3
AFE 4
(TLE901x)
CMU4
AFE 5
(TLE901x)
CMU5
AFE 6
(TLE901x)
CMU6
AFE n
(TLE901x)
CMU n
CAN
PMU
Pack Monitoring IC
CAN
5V
Microcontroller
Isolation
Transciever
CAN Transceiver
VCU
Microcontroller
Vpack
lpack
SOx pack = F(Vpack, Ipack, T)